##### NEW BILSTEIN B16 RIDECONTROL® SYSTEM FOR

##### MANY LATE MODEL BMW 3 and 5 SERIES

This new system from Bilstein, available for select models of 3 and 5 series BMWs, allows the driver to shift between a comfort oriented or a significantly firmer, aggressive performance damping mode with a simple push of the dash mounted button. The integrated control unit switches the damping settings on all four shocks/struts in fractions of a second to deliver the handling characteristics you desire. The shocks on this system use Bilstein’s inverted tube technology.

Originally designed for motorsports applications, Bilstein’s inverted tube technology utilizes the same technological design advantages as Bilstein gas pressure shock absorbers. The Bilstein monotube strut insert is installed with the piston rod at the base of the strut tube. Here the rod is completely protected from road contamination of any kind. The large wear-resistant

chromium tube moves up and down in friction bearings. This distributes the supporting and lateral forces over a wide area to provide exceptional stability. Bilstein's inverted struts are engineered to provide maximum performance characteristics along with exceptional driver comfort.

This new Bilstein ridecontrol® system has a MSRP of $3150.00, which includes the four electronically controlled shocks, control module, installation harness, and activation switch.

This system not only provide superior performance characteristics, but also comes with a lifetime aftermarket warranty. Bilstein designs and manufactures shocks for most cars, trucks and SUVs.

For more information, see your local

Bilstein dealer or visit:

www.bilstein.com

or call

1-800-537-1085

For downloadable electronic files go to

www.fallads.com and click on news/press

# Text boxes

##### News Release